M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles. Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings Interface also provides a routine carpet maintenance programme. For further information contact Interface’s Technical Department.

Net Effect B601 - Carpet Tiles

A tapestry tufted patterned structured loop pile manufactured from 100% recycled BCF solution dyed nylon, contains pre and post-consumer recycled content, with a Graphlex® backing.  Available in 8 colourways and carries a Class 33 heavy contract classification.  The 9.7mm thick tile is available in 500 x 500mm size as standard. Size options are available with minimum quantities.

Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral.  Consult with Interface for technical literature and to obtain samples.

Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: N/a. Carpet tiles to be adhered direct to the subfloor.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Net Effect – B601 Carpet Tiles

- Type: Tapestry tufted patterned structured loop pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC2

Size: 500 x 500mm standard size. 
Colour/pattern: 332904 Black Sea / 332905 North Sea / 332907 Arctic / 332906 Pacific / 332908 Atlantic / 332909 Caspian / 332910 Sand / 332911 Driftwood

Method of laying: Non-Directional

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300

Email: enquiries@interface.com     Web: www.interface.com