M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles. Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings Interface also provides a routine carpet maintenance programme, using the Image range of cleaning materials. For further information contact Interface’s Technical Department.

Chenille Warp Carpet Tiles

A tufted patterned level tip sheared pile tile manufactured from recycled solution dyed nylon with Graphlex® backing.
The range is available in 12 colourways and carries a Class 33 heavy contract classification.
The 6.6mm thick tiles are available in 500 x 500mm as standard, with size options available with minimum order quantities.

Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral.     
Consult with Interface for technical literature and to obtain samples.

Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: Should be laid where required over existing timber bases.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Chenille Warp Carpet Tiles

- Type: Tufted patterned level tip sheared pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC1

Size: 500 x 500mm standard size.

Colour/pattern: 309308 Retrospective / 309309 Nostalgia / 309310 Recurrence / 309311 Flash Back / 309312 Reflections / 309313 Repetitions / 309314 Recollections / 309315 Reminiscent / 309316 Total Recall / 309317 Yesterday / 309318 Hindsight / 309319 Remembrance

Method of laying: Brick, Ashlar and Quarter Turn.

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300,

Email: enquiries@interface.com     Web: www.interface.com