M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles. Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings Interface also provides a routine carpet maintenance programme, using the Image range of cleaning materials. For further information contact Interface’s Technical Department.

# Elevation II Carpet Tiles

A microtuft patterned level loop tile manufactured from 100% solution dyed nylon with Graphlex® backing.

The range is available in 16 colourways and carries a Class 33 heavy contract classification. The 4.8mm thick tiles are available in 500 x 500mm as standard.

Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral. Consult with Interface for technical literature and to obtain samples.

Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: Should be laid where required over existing timber bases.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Elevation II Carpet Tiles

- Type: Microtuft patterned level loop pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC2

Size: 500 x 500mm standard size

Colour/pattern:   307130 Lightgrey/307131 Greige/307134 Old Silver/307135 Linden Shade/307138 Carthusian/307139 Snake Charmer/307142 Charcoal/307143 Espresso/307132 Honey/307133 Olive/307136 Camelot/307137 Violet/307140 Paprika Blossom/307141 Summernight/307144 Cinema/307145 Touareg

Method of laying: Quarter Turn

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300,

Email: marketing@interface.com     Web: www.interface.com