M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles.  Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings, Interface also provides a routine carpet maintenance programme, using the Image range of cleaning materials. For further information contact Interface’s Technical Department.

Fastforward Carpet Tiles
A tufted plain level cut pile tile, manufactured from Recycled Solution Dyed Nylon with Graphlex® backing. Available in 8 colourways and carries a Class 33 heavy contract classification. The 5.4mm thick tile is available in 500 x 500mm size as standard. Size options are available with minimum quantities.
Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral. Consult with Interface for technical literature and to obtain samples.

Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: Should be laid where required over existing timber bases.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Fastforward Carpet Tiles

- Type: Tufted plain level cut pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC1

Size: 500 x 500mm standard size. 
Colour/pattern: 608120 Steel / 608121 Granite / 608122 Lead / 608123 Coffee /

608124 Iron / 608127 Mink / 608130 Copper / 608132 Slate

Method of laying: Brick, Ashlar and Non Directional

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300,

Email: enquiries@interface.com     Web: www.interface.com