M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles. Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings Interface also provides a routine carpet maintenance programme. For further information contact Interface’s Technical Department.

Monochrome

A tufted patterned structured loop pile manufactured from 100% recycled BCF solution dyed nylon, contains pre and post-consumer recycled content, with a Graphlex® backing.  Available in 48 colourways and carries a Class 33 heavy contract classification.  The 8.2mm thick tile is available in 500 x 500mm size as standard. Size options are available with minimum quantities.

Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral.  Consult with Interface for technical literature and to obtain samples.

Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: N/a. Carpet tiles to be adhered direct to the subfloor.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Monochrome

- Type: Tufted patterned structured loop pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC2

Size: 500 x 500mm standard size. 
Colour/pattern: 346690 Millstone / 346691 Platinum / 346692 Titanium / 346693 Felt / 346694 Storm / 346695 Seal / 346696 Carbon / 346697 Black / 346698 Silver / 346699 Surf / 346700 Jade / 346701 Jungle / 346702 Mercury / 346703 Flemish Blue / 346704 Pacific / 346705 Peacock / 346706 Lupin / 346707 Flag Blue / 346708 Lobelia / 346709 Nightshadow / 346710 Blue / 346711 Iris / 346712 Danube / 346713 Elderberry / 346714 Very Berry / 346715 Lilac Haze / 346716 Redwood / 346717 Damson / 346718 Orange / 346719 Gerbera / 346720 Terra Firma / 346721 Wine Berry / 346722 Malt / 346712 Putty / 346724 Rhino / 346725 Coffee Bean / 346726 Cream / 346727 Caraway / 346728 Briar / 346729 Havana / 346730 Barley / 346731 Castor / 346732 Papyrus / 346733 Bullrush / 346734 Spun Gold / 346735 Dandelion / 346736 Meadow / 346737 Yew

Method of laying: Monolithic

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300,

Email: enquiries@interface.com     Web: www.interface.com