M50 RUBBER/ PLASTICS/ CORK/ LINO/ CARPET TILING/ SHEETING
130 CARPET TILING:

Interface produces an extremely wide range of carpet tiles. Tiles are available with tufted cut and loop pile, fusion bonded cut pile and micro-tuft and multi-level pile. Carpet tiles conform to the requirements of BS EN 1307. In addition to the supply of floor coverings, Interface also provides a routine carpet maintenance programme, using the Image range of cleaning materials. For further information contact Interface’s Technical Department.

Microsfera
A Microtuft plain level loop pile tile, manufactured from 100% Polypropylene with Graphlex® backing. Available in 8 colourways and carries a Class 33 heavy contract classification. The tile is 3.6mm thick and is available in 500 x 500mm size as standard. Size options are available with minimum quantities.
Use our ReEntry service to take away existing Interface tiles which will be cleaned and repurposed through our ReEntry partners (Registered charities).

Simply add our Cool Carpet service to your order to make your purchase carbon neutral.  Consult with Interface for technical literature and to obtain samples.
 
Location: Heavy use areas. Office, retail, hospitality, leisure and educational areas.

Base: Please refer to Interface installation guide for details of suitability.

- Preparation: Subfloors should be prepared in accordance with BS 5325 or corresponding National and European Standards.

- Fabricated Underlay: N/a. Carpet tiles to be adhered direct to the subfloor.

Carpet Tiles:

- Manufacturer: Interface

- Product reference: Microsfera

- Type: Microtuft plain level loop pile

BS EN 1307 classification:

- Category: Type 1

- Level of use class: Heavy Contract 33

- Luxury rating class: LC1

Size: 500 x 500mm standard size.
Colour/pattern: 4173001 Black/ 4173002 Grey/ 4173003 Warm Grey/ 4173004 Greige/ 4173005 Brown/ 4173006 Copper/ 4173007 Chinese Blue/ 4173008 Light Blue

Method of laying: Quarter Turn

Interface Europe Ltd., Shelf Mills, Shelf, Halifax, West Yorkshire HX3 7PA

Tel: 01274 690690, Fax: 01274 694095.

Customer Services Tel: 08705 304030, Fax: 01274 698300,

Email: enquiries@interface.com     Web: www.interface.com